## Slide 1: Evaluation of 2015 SDG&E Commercial Thermostat Program
2016 PLMA Spring Conference
Smart Thermostat Interest Group Workshop
May 10, 2016
Prepared by:
Josh Schellenberg, Principal
Dan Thompson, Project Analyst

## Slide 2: Overview
Program Overview
Ex Post Methodology
Ex Post Results
Ex Ante Methodology
Enrollment Forecast
Ex Ante Results
Additional Findings
Recommendations

## Slide 3: Program Overview

## Slide 4: The San Diego Gas & Electric (SDG&E) Commercial Thermostat program is a growing AC load control program
Smart thermostat installations are used for AC load control demand response in SDG&E’s service territory
1,243 small and medium business (SMB) customers (11,292 thermostats) participated in 2015 DR events
1,079 commercially managed residential customers (1,130 thermostats) participated in 2015 DR events
Two primary load control strategies:
  50% cycling
  4-degree setback
Any participant can override the load control at any point
Hours of Availability | Hours of Actual Use | Number of Available Dispatches | Number of Actual Dispatches
72 hours | 16 hours | 18 events | 4 events

## Slide 5: Ex Post Methodology

## Slide 6: Impacts were estimated using matching with difference-in-differences regression and same-day adjustment
Chart: Hour Ending
Participants | 19.8399 | 19.1498 | 18.68 | 18.4869 | 18.6178 | 20.4596 | 24.3021 | 30.6885 | 36.1394 | 39.2823 | 42.0015 | 43.2538 | 43.6813 | 44.3093 | 40.3308 | 38.7017 | 36.1785 | 33.4862 | 32.515 | 31.2985 | 29.2361 | 26.5329 | 23.8502 | 21.7343
Control | 20.7444 | 19.9203 | 19.2455 | 19.0756 | 19.6641 | 21.3661 | 24.9465 | 29.4493 | 34.3206 | 37.485 | 39.8794 | 41.4886 | 41.9103 | 42.0562 | 41.1804 | 38.6841 | 35.7577 | 33.7132 | 31.5885 | 30.9932 | 29.7344 | 27.6631 | 24.7549 | 22.9282
Reference | 19.8964 | 19.009 | 18.6252 | 18.5518 | 18.6851 | 20.3736 | 23.8459 | 29.512 | 34.6575 | 39.7296 | 41.9683 | 43.1505 | 43.6292 | 44.0507 | 43.4368 | 41.0974 | 38.4181 | 35.6947 | 33.1619 | 30.3812 | 28.9734 | 26.5056 | 23.761 | 21.9187
The matching algorithm selects control customers with a similar load profile to participants.
The regression adjusts for differences remaining after matching.

## Slide 7: Ex Post Results

## Slide 8: The average 2015 event day impact was 2.49 kW per customer and 0.27 kW per thermostat for commercial customers

## Slide 9: The per thermostat impacts for commercial customers remained relatively constant in percent terms after the first event hour.
Chart: Hour Ending
| 0.625 | 0.66666666666666663 | 0.70833333333333337 | 0.75
Impact per Thermostat | 0.34191 | 0.26371 | 0.24654 | 0.2431
Impact (%) | 0.071508 | 0.058293 | 0.058297 | 0.06187

## Slide 10: The relationship between weather and impacts was not detectable given the sample sizes and consecutive events.
Chart: Event
| Aug 28, 2015 | Sep 9, 2015 | Sep 10, 2015 | Sep 11, 2015 | Average Event
Impact per Thermostat | 0.15635 | 0.2776 | 0.32997 | 0.33134 | 0.27382
Mean17 | 82.2244 | 86.4597 | 85.2358 | 82.6419 | 84.1404
Three of the four events were on consecutive days

## Slide 11: A small number of thermostats installed in commercially-operated residences returned smaller and noisier impacts.
Chart: Event
| Aug 28, 2015 | Sep 9, 2015 | Sep 10, 2015 | Sep 11, 2015 | Average Event
Impact per Thermostat | 0.028666 | 0.11144 | 0.14675 | 0.11733 | 0.10104
Mean17 | 80.9049 | 85.1402 | 84.4112 | 81.5698 | 83.0065

## Slide 12: The impact of the commercial thermostat program during SDG&E and CAISO system peaks were 3.02 MW and 3.44 MW, respectively
SDG&E system peak
  September 9th
  Between 3 PM and 4 PM (3:43 PM)
  Commercial Thermostat impact: 3.02 MW
CAISO system peak
  September 10th
  Between 4 PM and 5 PM (4:53 PM)
  Commercial Thermostat impact: 3.44 MW

## Slide 13: Ex Ante Methodology

## Slide 14: Ex Ante impacts were calculated by combining 2015 per-thermostat impacts with Summer Saver weather sensitivity
Ex post estimates were developed with the key output being the average per-thermostat impact (0.27 kW)
Regression models were estimated that relate hourly usage to weather
A regression model was estimated that relates the Summer Saver 50% cycling impacts to temperatures using five years of events
Summer Saver impacts were predicted for the ex ante weather scenarios using the model in step 3
The ratio of impacts to weather observed in the Summer Saver program was applied to the per-thermostat impact (step 1) for the commercial thermostat program

## Slide 15: Enrollment Forecast

## Slide 16: The Commercial Thermostat program is expected to grow by 17%
Chart: Year
| 2015 | 2016 | 2017 | 2018-2026
Commercial (CPP) | 11136.33 | 11946.73 | 11932.11 | 11525.75
Commercial (Non CPP) | 934.2836 | 1683.799 | 3283.367 | 4090.131
Residential | 1130.041 | 1130.041 | 1130.041 | 1130.041

## Slide 17: Ex Ante Impacts

## Slide 18: The per-customer impacts are expected to increase ~5%
The August CAISO 1-in-2 day is hotter than the August SDG&E 1-in-2 day.
The per-customer impact changes over time due to small changes in the customer mix.
Chart: Year
| 2016 | 2017 | 2018-2026
Impact (SDG&E) | 0.94682 | 0.98284 | 0.99259
Impact (CAISO) | 1.0207 | 1.0598 | 1.0704
Enrolled Thermostats | 14560.37 | 16245.42 | 16745.92

## Slide 19: The aggregate impacts are expected to increase by ~15%
The aggregate impact changes for the same reasons as above.
It also changes due to increasing enrollment.
Chart: Year
| 2016 | 2017 | 2018-2026
Impact (SDG&E) | 2.546 | 2.8414 | 2.9291
Impact (CAISO) | 2.7447 | 3.0639 | 3.1587
Enrolled Thermostats | 14560.37 | 16245.42 | 16745.92

## Slide 20: The aggregate ex post impacts increased while the 2017 ex ante impacts decreased from the 2014 evaluation to the 2015 evaluation
Aggregate ex post impacts increased by nearly 4.5 times from 2014 to 2015 due to:
  378% increase in enrolled thermostats
  1.2 degree increase in average event temperatures
Ex Ante estimates for 2017 fell from the 2014 to the 2015 evaluation due to:
  18% drop in projected enrollment
  0.7 degree drop in average temperatures
 | Evaluation Year | Aggregate Impact (MW) | Thermostats Enrolled | Mean17
Ex Post | 2014 | 0.7 | 3,282 | 82.9
 | 2015 | 3.1 | 12,422 | 84.1
Ex Ante (2017) | 2014 | 3.41 | 19,973 | 75.6
 | 2015 | 2.84 | 16,346 | 74.9

## Slide 21: Additional Findings

## Slide 22: 2015 impacts per thermostat throughout the event hours were very similar for each load control strategy
Chart: Event Hour
| 2-3 PM | 3-4 PM | 4-5 PM | 5-6 PM | Overall
4-Degree Setback | 0.34491 | 0.23527 | 0.20558 | 0.19984 | 0.2464
50% Cycling | 0.33983 | 0.2367 | 0.21245 | 0.18974 | 0.24468

## Slide 23: Smart thermostats delivered the largest impacts for retail customers; hotels underperformed relative to other industries
Chart: Industry
| Hotels | Institutional | Offices, Finance, Restaurants, Services | Retail Stores | Schools | All Industries
Avg. Thermostat Impact (kW) | 0.02 | 0.26 | 0.34 | 0.46 | 0.34 | 0.27
Avg. Thermostat Impact (kW) | 0.02 | 0.26 | 0.34 | 0.46 | 0.34 | 0.27
There variance in performance across industries is high.

## Slide 24: Energy savings ranged from 2% to 4% of whole-building electricity usage, 1.7 kWh per day per thermostat (620 kWh per year)
Chart: Months Since Installation
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Participant Count | 1230 | 1146 | 1121 | 1086 | 1058 | 987 | 970 | 903 | 872 | 832 | 767 | 574
Regression-Estimated Reference | 421.1231 | 434.927 | 426.2618 | 423.6205 | 426.709 | 451.5525 | 437.9894 | 454.9664 | 476.7555 | 478.7436 | 470.3893 | 432.2081
Participant | 411.3335 | 420.6833 | 408.9769 | 409.6416 | 411.7981 | 437.4294 | 425.4889 | 441.2156 | 464.2997 | 464.3428 | 459.2707 | 413.2128
95% Confidence Interval | 429.2184 | 443.0307 | 434.4174 | 431.3679 | 435.4225 | 460.352 | 446.8871 | 463.8357 | 487.1516 | 489.3065 | 480.6667 | 444.3132
lower | 413.0278 | 426.8234 | 418.1063 | 415.873 | 417.9955 | 442.7529 | 429.0918 | 446.0971 | 466.3594 | 468.1807 | 460.1118 | 420.1029

## Slide 25: Energy savings in the peak period (2-6 PM) during the summer on non-event weekdays by industry
Chart: Industry
| Hotels | Institutional | Offices, Finance, Restaurants, Services | Retail Stores | Schools
DR Impact | 0.02 | 0.26 | 0.34 | 0.46 | 0.34
Total Impact | 0.09 | 0.41 | 0.51 | 0.39 | 0.22
DR Impact | 0.02 | 0.26 | 0.34 | 0.46 | 0.34
Total Impact | 0.09 | 0.41 | 0.51 | 0.39 | 0.22

## Slide 26: Discussion

## Slide 27
Nexant, Inc. 101 Second St., 10th Floor San Francisco, CA 94105 415-369-1000
For comments or questions, contact: Josh Schellenberg Principal jschellenberg@nexant.com
Dan Thompson Project Analyst dthompson@nexant.com